## Slide 1: The Effect of Microgravity on the Use of Cactus Mucilage for Water Purification
By: Jesus Castor
and
Naiki Armendariz
Mentor:
Dr. Gertrud Konings
El Paso Community College

## Slide 2: Background
Cactus was already used by 19th century Mexican communities to purify water
Dr. Norma Alcantar’s research at the University of South Florida proved that mucilage can remove arsenic and iron from water

## Slide 3: Experiment’s Rationale
Chromium was chosen because of its presence on moon’s surface besides iron
Therefore steel production on the moon is being considered
Chromium-VI would be produced as a waste and could contaminate moon water
The mucilage of the Prickly Pear, Opuntia ficus indica, an edible cactus, can be a solution to chromium removal from contaminated water

## Slide 4: Objective
Test the effect of microgravity on the mucilage’s ability of removing heavy metals, in particular chromium-VI

## Slide 5: Composition of Cactus Mucilage
Cactus mucilage is the clear slimy fluid secreted when a stem segment (cladode) is damaged
The main component of the Gelling Extract (GE) mucilage is a pectin
Pectins are found between the cells and in the cell walls of most plants

## Slide 6: Purification Property of Mucilage
When extraced, GE pectin is covered by a layer of Ca2+ ions.
When chromium-VI reacts with the pectin, Cr6+ displaces Ca2+ ions, giving the pectin an outside layer of Cr6+ ions.
When chromium-VI binds to pectin, a greater and heavier flock is formed, which sediments to the bottom under Earth’s gravity conditions, leaving the water in the middle free of chromium-VI.

## Slide 7: Hypothesis
Microgravity should not affect the chromium binding, since the binding is an ionic reaction. Thus the purification process is expected to work

## Slide 8: Experiment Design
Chromium-6 trioxide (CrO3) (1.00 mg/L) dissolved in distilled water (H2O): Experiment volume filled to capacity, approx. 6.28 ml
FME Main Volume
O. ficus-indica mucilage extract (10mg/L mucilage in distilled water): filled to capacity, approx. 0.92 ml
Short Ampoule A
100% Ethanol (stabilizing agent): filled to capacity, approx. 0.92 ml
Short Ampoule B

## Slide 9: 1st Experiment
  Cube of cactus placed in 1.00 mg/L chromium solution for two weeks, then rinsed several times in alcohol
Cactus piece observed under the HITACHI TM-1000 Scanning Electron Microscope (SEM) and measured in X-ray acquisition

## Slide 10: 2nd Experiment
2 ml of liquified cactus + 2ml of 1.00 mg/L chromium solution + 2ml of 100 % alcohol
After one day, solution measured in a HACH DR 2800 spectrophotometer
2nd Experiment | 
Chromium VI concentration | 
Control | 0.428 mg/L
mucilage | 0.149 mg/L
Difference Percentage | 65.19%

## Slide 11: 3rd Experiment
Flight experiment trial: 6.3 ml of 1.00 mg/l chromium, 0.92 ml mucilage, and 0.92 ml of 100% alcohol
Wait seven days to add alcohol and read solution in HACH DR 2800 spectrophotometer
Parallel experiments with several concentrations of mucilage

## Slide 12: 4th Experiment
6.3 ml of 1.0 mg/l of Cr-VI solution + 0.92 ml of mucilage (different concentrations) + 0.92 of 100% ethanol
Solution measured directly from the test tube and after filtration to remove mucilage

## Slide 13: 4th Experiment cont.
6.3 ml of 1.0 mg/l of Cr-VI solution + 0.92 ml of mucilage + 0.92 of 100% ethanol
Solution measured directly from the test tube and after centrifugation

## Slide 14: Conclusions
From the experiments performed the final design of the flight experiment was determined: 10 mg/l GE mucilage will be used and the mucilage will be filtered out of the solution before measurement
Still waiting to get our experiment back from space

## Slide 15
Jesus Castor[1], Naiki Armendariz[1], Dr. Gertrud Konings[1], Dr. Maria Arteaga[1], Dr. Norma A. Alcantar [2], Dr. Alfonso Bencomo[3]
1.-RISE program, El Paso Community College, El Paso, TX 79925, USA
2.-Department of Chemical and Biomedical Engineering, University of South Florida, Tampa, FL 33620, USA
3.-Departamento de Investigación de Genética Humana, Universidad Autónoma de Guadalajara, Guadalajara, Jalisco 44100, MX
Student Team Members
Co-principal investigators & collaborators

## Slide 16: Financial Support
Texas Space Grant Consortium, Austin, Texas
NIH MBRS-RISE (Research Initiative for Scientific Enhancement) Grant #5R256M060424
El Paso Community College
A special Thank-You to all our supporters, especially also to Jeff Goldstein and Harri Vanhalla for making this project possible.